## Slide 1
DIGITAL SIGNAL PROCESSING | COURSE PROJECT
Signal Jamming Detection
& Analysis System
SJDAS — v2.4.1
Submitted to:
Eng. Shimaa Sherif
GROUP B1
Student Name
Student ID
Alaa Ali Elashker
2401569
Jana Ahmed Elzamzamy
2401507
Esraa Mohsen Samir
2401532
Zahraa Reda Mohamed
2401422

## Slide 2
OVERVIEW
What is SJDAS?
SJDAS is a complete real-time system for detecting and analyzing radio signal jamming. It applies Digital Signal Processing (DSP) techniques to continuously monitor signal quality and trigger instant alerts when jamming is detected.
📡
Signal Generation
Pure configurable sine wave synthesis
🔊
Jamming Simulation
AWGN — Additive White Gaussian Noise
📊
FFT Analysis
Fast Fourier Transform power spectrum
🚨
Auto Detection
SNR threshold with severity grading

## Slide 3
ARCHITECTURE
Project Architecture
⚙️ main.py
Application Entry Point
Window layout · Monitoring loop · Module coordination · Threading
🧮 dsp_engine.py
Core DSP Pipeline
Signal generation · FFT · SNR calculation · Jamming detection
📈 visualizer.py
Real-Time Plots
Time domain & frequency domain plots · Matplotlib + Blit rendering
🖥️ ui_components.py
UI Dashboard
Control panel · Metrics display · Alert banners · CustomTkinter
⚡ Threading Model: DSP processing runs on a Background Thread — UI updates are scheduled on the Main Thread via .after() to ensure full interface responsiveness

## Slide 4
DSP & TELECOM
How DSP Serves Telecommunications
📡 Telecommunications Field
▸ Information is transmitted via radio waves
▸ Signals are corrupted by noise & interference
▸ Systems must constantly monitor signal quality
▸ SNR is the key metric for communication quality
▸ FFT is used in every modern receiver station
▸ Electronic jamming is a real threat (EW)
🧮 Digital Signal Processing
▸ Convert analog signals to digital (ADC)
▸ Apply mathematical algorithms to signals
▸ Analyze frequency spectrum with FFT
▸ Compute signal power and noise power
▸ Detect anomalous patterns automatically
▸ Process data in real time (low latency)
⟺
✦ SJDAS bridges both fields: DSP algorithms are applied to solve a real telecommunications problem — detecting and preventing signal jamming.

## Slide 5
DSP CONCEPT #1
Signal Generation & Nyquist Theorem
x(t) = A · sin(2π · f · t)
A
Amplitude
Signal strength — range 0.1 to 5.0 V, adjustable
f
Frequency
Carrier frequency — 10 to 500 Hz configurable
t
Time Axis
1000 sample points over a 500 ms window
📐 Nyquist-Shannon Sampling Theorem
fs > 2 × f_max → 2000 Hz > 2 × 1000 Hz ✓
The sample rate (fs = 2000 Hz) must exceed twice the highest signal frequency to avoid Aliasing — a distortion artifact that corrupts the reconstructed signal.
# Signal generation in dsp_engine.py
clean_signal = amp * np.sin(2 * np.pi * freq * time_axis)

## Slide 6
DSP CONCEPT #2
Jamming Simulation — Additive White Gaussian Noise
y(t) = x(t) + η(t) η ~ N(0, σ²)
What is AWGN?
◆ Random distribution with zero mean (μ = 0)
◆ Models real-world electronic jamming
◆ Present in every real communication channel
◆ σ (std deviation) controls jamming intensity
◆ Higher σ → more noise → lower SNR
🔵 Clean Signal (no jamming)
x(t) = 1.0 · sin(2π · 100 · t)
Perfect sine waveform | SNR = ∞
🔴 Jammed Signal (AWGN added)
y(t) = x(t) + N(0, σ²)
Original signal buried under noise
SNR drops below threshold → ALERT!
noise = np.random.normal(loc=0.0, scale=noise_sigma, size=n_samples) # AWGN
jammed_signal = clean_signal + noise

## Slide 7
DSP CONCEPT #3
FFT Analysis — Fast Fourier Transform
X[k] = Σ x[n] · e^(−j·2π·k·n/N) P[k] = |X[k]|² / N
01
Time → Frequency
→ Take 1000 samples of the signal
→ Apply rfft() to get frequency data
→ Output: complex coefficients X[k]
02
Power Spectrum
→ P[k] = |X[k]|² / N
→ Convert to dB: 10·log₁₀(P)
→ Reveals dominant frequency in signal
03
Peak Detection
→ Find highest value in spectrum
→ Peak frequency = carrier frequency
→ Deviation reveals jamming presence
💡 Why rfft() instead of fft()? → Real-valued signals have symmetric spectra — rfft() returns only N/2+1 positive frequencies, cutting computation by 50%
fft_jammed = np.fft.rfft(jammed_signal) | power = (np.abs(fft_jammed)**2) / n_samples | psd_db = 10*np.log10(power + 1e-12)

## Slide 8
DSP CONCEPT #4 & #5
SNR Calculation & Jamming Detection
SNR = 10 · log₁₀ (P_signal / P_noise)
IF SNR (dB) < Threshold → JAMMING ⚠
🎯 Severity Classification
NONE
SNR ≥ Threshold
No jamming — clean signal
LOW
Deficit < 5 dB
Mild jamming — signal still readable
MEDIUM
5 – 15 dB
Moderate jamming — noticeable degradation
HIGH
15 – 30 dB
Severe jamming — reception difficult
CRITICAL
Deficit > 30 dB
Total jamming — signal lost
📊 Confidence Score
The system computes a % confidence score for every jamming detection decision:
0%
Perfectly clean signal
50%
Possible jamming
100%
Confirmed jamming
📈 Exponential Moving Average
α=0.25 smoothing applied to SNR readings to reduce measurement noise
signal_power = np.mean(clean_signal**2) | noise_power = np.mean(noise**2)
snr_db = 10 * np.log10(signal_power / max(noise_power, 1e-12)) # → jamming_detected = snr_db < threshold

## Slide 9
SYSTEM PIPELINE
Complete DSP Pipeline — Real-Time Flow
1
Signal Generation
Sine wave synthesis
x(t) = A·sin(2πft)
→
2
AWGN Injection
Add Gaussian noise
y(t) = x(t) + N(0,σ²)
→
3
FFT Transform
Frequency analysis
X[k] = FFT(y[n])
→
4
SNR Calculation
Signal-to-noise ratio
SNR = 10·log₁₀(Ps/Pn)
→
5
Detection & Alert
Threshold comparison
SNR < threshold → ALERT
⏱️ Update Rate
80 ms / frame = ~12.5 FPS → Smooth real-time display without CPU overload
🔀 Threading Model
DSP Thread (Background) + UI Thread (Main) → Full interface responsiveness

## Slide 10
CONCLUSION
What Did This Project Achieve?
🎓 Practical DSP Application
Translated FFT, SNR, and noise theory from textbooks into working, real-time Python code
📡 Connecting Field to Problem
Simulated a real telecom challenge — electronic jamming — and built a system to detect it
⚡ Real-Time System Design
Achieved 12.5 FPS processing with multi-threading and matplotlib blit for optimized performance
🏗️ Sound Software Engineering
Modular 4-file architecture: each component is independent, testable, and extensible
SJDAS proves that DSP is more than theory — it is a powerful engine for building intelligent communication systems capable of real-time detection and response to electronic jamming in real-world environments.